## Slide 1: Intro to Network Protocols
NETPIE R&D TEAM
NECTEC

## Slide 2: TCP/IP Communication

## Slide 3: TCP/IP
Application Layer
Transport Layer
Internet Layer
Data Link Layer
Physical Layer
HTTP, HTTPS, FTP, Mail, DNS, MQTT
TCP, UDP
IPv4, IPv6
Ethernet, WiFi, Bluetooth, Zigbee, …
Copper, Fiber, Satellite, Wireless, …

## Slide 4: IoT Application-Layer Protocols
MQTT
HTTP
AMQP
CoAP
NETPIE Supports

## Slide 5: HTTP client-server model

## Slide 6: HTTP (Web)
Web Server
HTTP Request
HTTP Response
HTTP Request
HTTP Response
Web page
Web page

## Slide 7: HTTP
Server
HTTP Request
HTTP Response
HTTP Request
HTTP Response

## Slide 8: HTTP
Server
HTTP Request
HTTP Response
HTTP Request
HTTP Response
22 C
22 C

## Slide 9: MQTT publish-subscribe model

## Slide 10: MQTT

## Slide 11: MQTT Routing – Topic based
myhome/floor1/
bedroom/temp
myhome/floor1/
bedroom/temp
myhome/floor1/bedroom/temp

## Slide 12: MQTT – Retained Messages
22 C
Retain = True
22 C
A MQTT client can publish a retained message by setting
Retain Flag to True in the PUBLISH packet.

## Slide 13: MQTT – Retained Messages
22 C
A client who subscribes to a topic with a
retained message would get sent the message
immediately after subscription.

## Slide 14: MQTT – Last Will
A client can establish the connection
with the broker with “last will” message
attached to its CONNECT packet.
Unwillingly
disconnected!!!

## Slide 15: MQTT – Last Will
When it is disconnected unintentionally,
the broker will publish its last will to
the other clients.
Last will
Last will

## Slide 16: Why MQTT
Asynchronous communication
Small code footprint
Saving network bandwidth – small header

## Slide 17: MQTT - QoS
QoS 0 – At most once
    Least reliable
    Fastest
    No acknowledgment
QoS 1 – At least once
    One loop of acknowledgment
QoS 2 – Exactly once
    Most reliable
    Slowest with the largest headers
    Two loops of acknowlegment